## Slide 1: Balancing Robot
By: Sophie Turner & Taylor Nakai

## Slide 2: Balancing Robot Parts
Arduino Uno (mainly the atmega328p)
MPU 6050
2 - NEMA Stepper Motors
2 - A4988 Stepper Motor Drivers
3- 3.7 Lipo Batteries
Lipo Battery Cartridge
2-Wheels
2-3 Acrylic Plastic Platforms
4 Rods
Breadboard
1-100uF Capacitor
Open-Smart Transceiver (Transmitter and Receiver)
Notes: Stepper motors are precise and have no performance loss when the battery voltage drops

## Slide 3: 3D Printed Parts
Motor Mounts
Adapters to connect wheels to motors
Battery Mount
Bracket Holders
Motor Mounts
Adapters to connect wheels to motors
Bracket Holders

## Slide 4: Building Robot Frame
2 acrylic plastic rectangular platforms with holes in the corners
4 threaded rods
16 hex nuts

## Slide 5: PCB Schematic Design

## Slide 6: PCB Layout Design

## Slide 7: Fabricated and Soldered PCB

## Slide 8: Code Overview
Modified version of Joop Brokking’s code
Code allows for interrupt service routine (ISR) so two tasks can run simultaneously
  Receive data from MPU6050
  Manage PID controller
Triggers the interrupt every 20us to update PID
Uses MPU6050’s accelerometer and gyro information to calculate angle to help robot balance

## Slide 9: Setting the acc_calibration_value
Used modified code given by Dr. Li
Acc_calibration_value needed to be set by user
Based off offset of the MPU
Going through Joop Brokking tutorial, found hardware test code that gave acc_calibration_value value
A critical variable associated with the code

## Slide 10: Calibrating the PID Values
Values that worked for us
  p_gain = 55;
  I_gain = 0;
  d_gain = 10;
Determined pid gain values by trial and error
Used serial monitor to test the pid_output variable and adjusted if needed

## Slide 11: Balancing Car Demonstration

## Slide 12: Future Plans
Implement the PCB instead of the breadboard circuit
Implement the joystick to control movement of robot
Refactor code